## Slide 1: Ch6. Programming for Humans Terminal Control and Signals
ELEC462003 System Programming

## Slide 2: Objectives
Ideas and Skills
  Reading and changing settings of the terminal driver
  Modes of the terminal driver
  Nonblocking input
  Timeouts on user input
  Introduction to signals: How Ctrl-C works
System Calls
  fcntl
  signal

## Slide 3: Device-Specific Programs
Device-Specific Programs : interact with specific devices
  Ex: Programs to control scanners and printers, take photographs, and handling some I/O devices
In this chapter, we explore the ideas and techniques of writing device-specific programs by looking at programs that interact with terminals.
Notes: We refer to these terminal-oriented programs as user programs.

## Slide 4: User Programs: A Common Type of Device-Specific Program
Ex:
  vi, emacs, and many of the games
These programs adjust settings in the terminal driver to control how keystrokes are handled and output is produced.
Common concerns of user programs using the terminal include:
  Immediate response to keys
  Immited input set
  Timeout on input
  Resistance to Ctrl-C
Notes: We shall learn about these topics by writing a program that implements all these features.
Lynx is a customizable text-based web browser for use on cursor-addressable character cell terminals.
Pine is a freeware, text-based email client

## Slide 5: Contents
6.1 Software Tools vs. Device-Specific Programs
6.2 Modes of the Terminal Driver
6.3 Writing a User Program: play-again.c
6.4 Signals
6.5 Prepared for Signals: play_again4.c

## Slide 6: Ex1: A short translation program
Notes: Explore the driver in detail by experimenting with a shot translation program

## Slide 7: Canonical Mode: Buffering and Editing
Run the program using the default settings:
The rotate program does none of these operation: buffering, echoing, editing, control key processing are all done by the terminal driver
$ gcc rotate.c -o rotate
$ ./rotate
abx  cd
bcde
efg
$
back space
Terminal Driver
Ctrl+C
Notes: TeCanonical Mode: Buffering and Editing

## Slide 8: Noncanonical Processing
Turning off canonical mode processing in the driver
^C
Turning off canonical mode processing and echo mode in the driver
Notes: canonical processing = buffering+ editing

## Slide 9: Summary of Terminal Modes
canonical mode
  Buffering and editing are turned on
  terminal input is processed in lines terminated by newline ( '\n’ ) or EOF (Ctrl+D) characters.
noncanonical mode
  Buffering and editing are turned off
  But, terminal driver still does specific processing : ^C, \n, \r
non-anything mode : raw mode
  When all processing is turned off, the driver passes input directly to the program
Notes: PKA: an acronym for Previously Known As
※ $ stty –a
… erase = ^? ( or ^H) ; werase = ^W; kill = ^U …
The terminal can be placed into "raw" mode where the characters are not processed by the terminal driver,
but are sent straight through
(it can be set that INTR and QUIT characters are still processed).
This allows programs like emacs and vi to use the entire screen more easily.
※ When you design a user program for Unix, you need to decide which terminal mode matches the application.

## Slide 10: Contents
6.1 Software Tools vs. Device-Specific Programs
6.2 Modes of the Terminal Driver
6.3 Writing a User Program: play-again.c
6.4 Signals
6.5 Prepared for Signals: play_again4.c

## Slide 11: A shell script for a bank machine (ATM)
does the work of the ATM
obtains a yes or no answer from the user
Notes: fi : endif in shell
A shell script is a computer program designed to be run by the Unix shell, a command-line interpreter.

## Slide 12: Ex2: play_again.c
It obtains a yes or no answer from the user
The logic:
Prompt user with question
Accept input
If “y”, return 0
If “n”, return 1

## Slide 13: Ex2: play_again0.c
It obtains a yes or no answer from the user

## Slide 14: Ex2: play_again0.c
Two Problems caused by running in canonical mode
  User has to press the Enter key
  Program receives and processes an entire line of data when the user presses Enter.
First improvement: Turning off canonical input

## Slide 15: Ex3: play_again1.c – immediate response

## Slide 16: Ex3: play_again1.c – immediate response

## Slide 17: Ex3: play_again1.c – immediate response
// “c_cc” member : the control character array
// VMIN : tells the driver how many characters at a time we are reading

## Slide 18: Ex3: play_again1.c – immediate response
play_again1 receives and processes characters as they are typed without waiting for the Enter key!
$ gcc play_again1.c –o play_again1
Notes: play_again1 receives and processes characters as they are typed without waiting for the Enter key!

## Slide 19: Ex4: play_again2.c – ignore illegal keys
Notes: complaining about every character is annoying
turn off echo mode and discard characters until we get accetable input

## Slide 20: Ex4: play_again2.c – ignore illegal keys
Notes: complaining about every character is annoying
turn off echo mode and discard characters until we get accetable input

## Slide 21: Ex4: play_again2.c – ignore illegal keys
Compile and try this program: (no echo)
  Only when you press ”y” or “n” does the program return.
It needs one more feature;
  What if this program were used at a real ATM and a customer wandered away without pressing y or n?
  User programs are more secure when they include a timeout feature.

## Slide 22: Nonblocking Input: play_again3.c
We create this timeout feature by telling the terminal driver not to wait for input.
  If a program find no input, it sleeps a few seconds then look again for input.
  After three tries, the program give up

## Slide 23: Blocking vs. Nonblocking Input
When a program call getchar() or read() to read data from a file descriptor, the call waits for input: blocked
How do we turn off input blocking?
  Use fcntl() or open() to enable nonblocking input for a file descriptor.
Internally, nonblocking operation is pretty simple.
  Each file has a space to hold available unread data, inside the driver.
  If the fd has the O_NDELAY bit set and that space is empty, the read() returns 0.
Notes: * fcntl : manipulate fd
* Blocking is a property of any open file, not only connections to the terminals
We turn off blocking on a file descriptor and call read()
  If input is available, read() gets it and returns the number of characters it got.
  If no characters are available, read() returns 0, just as it does at end of file.
  If there is an error, read() returns -1
Internally, nonblocking operation is pretty simple.
  Each file has a space to hold available unread data, inside the driver.
  If the file descriptor has the O_NDELAY bit set and that space is empty, the read()returns 0.

## Slide 24: Ex5: play_again3.c – use nonblocking mode for timeouts
Notes:     Play_again3 uses fcntl to turn on the O_NDELAY flag for the file descriptor.
    (You can use the O_NONBLOCK bit.)

## Slide 25: Ex5: play_again3.c – use nonblocking mode for timeouts
※ returns a pointer to the first occurrence of the character c in the string s
Notes:     Play_again3 uses fcntl to turn on the O_NDELAY flag for the file descriptor.
    (You can use the O_NONBLOCK bit.)

## Slide 26: Ex5: play_again3.c – use nonblocking mode for timeouts

## Slide 27: Ex5: play_again3.c – use nonblocking mode for timeouts

## Slide 28: Ex5: play_again3.c – use nonblocking mode for timeouts
Small Problems with play_again3:
  The program sleeps for two seconds before calling getchar() to give the user a chance to type something.
    If the user types within one second,
      The program does not get the character until two seconds pass
  Without the call to fflush() after printing the prompt, the prompt does not appear until the program calls getchar();
    Why?
      The driver buffers output until it receives a newline or until the program tries to read from the terminal
Notes: The driver also line-buffer output;
The driver buffers output until it receives a newline or until the program tries to read from the terminal.
fflush: If the given stream was open for writing
any unwritten data in its output buffer is written to the file.

## Slide 29: Ex5: play_again3.c – use nonblocking mode for timeouts
A Big Problem: What happens if the user presses Ctrl-C?
※ The program is killed and
the entire login session is also killed!

## Slide 30: Ex5: play_again3.c – use nonblocking mode for timeouts
How did it happen?
  The program is killed without restoring the state of the terminal driver
    The terminals still in nonblocking mode when the shell returns to print its prompt and get a command line from the user.
    The shell calls read() to get the command line, but read(), operating in nonblocking mode, returns 0 immediately
How to protect our program from Ctrl-C?
Notes:   The terminals still in nonblocking mode when the shell returns to print its prompt and get a command line from the user.
  The shell calls read to get the command line, but read, operating in nonblocking mode, returns 0 immediately.

## Slide 31: Contents
6.1 Software Tools vs. Device-Specific Programs
6.2 Modes of the Terminal Driver
6.3 Writing a User Program: play-again.c
6.4 Signals
6.5 Prepared for Signals: play_again4.c
Notes: Next project : How to protect our program from Crtl-C?
Ctrl-C interrupts the current running pg.
This interruption is produced by a kernel mechanism, called signal

## Slide 32: What Does Ctrl-C Do?
The Ctrl-C key interrupts the currently running program
This interruption is produced by a kernel mechanism called a signal
Notes: Ctrl-C key interrupts the currently running pg. This interruption is produced by a kernel mechanism called a "signal“
VINTR (003, ETX, Ctrl-C, or also 0177, DEL, rubout) Interrupt character (INTR).
Send a SIGINT signal. Recognized when ISIG is set, and then not passed as input.
Ctrl-C interrupts the current running pg. This interruption is produced by a kernel mechanism, called signal

## Slide 33: What is a Signal?
A signal is a one-word message from kernel to process
  Each signal has a numerical code (e.g., interrupt signal is code number 2)
  When pressing the Ctrl-C key, kernel send the interrupt signal to the currently running process
Requests for signals come from three sources :
  Signals from user, ex) when user press Ctrl-C key
  Signals from kernel, ex) when the process does something wrong such as process exception and segmentation violation
  Signals from other processes, ex) a process can send a signal to communicate with other processes
Notes: Ctrl+C : u ask the kernel to send the interrupt signal to the current running process
A signal is a short message sent from the kernel to a process. Users, other processes, and the kernel itself may request a signal.

## Slide 34: Where Can I Find a List of Signals?
/usr/include/bits/signum.h
Notes: What do signals do? It depends. Many signals causes processes to die.

## Slide 35: What Can a Process Do about a Signal?
A process does not have to die when it receives SIGINT
A process can tell the kernel by using the signal(), how it wants to respond to a signal
A process has three choices:
  Accept the default action (usually death) signal(SIGINT, SIG_DFL);
  Ignore the signal signal(SIGINT, SIG_IGN);
  Call a function signal(signum, functionname);
Notes: a process does not have to die when it receives SIGINT
Does not have to use signal to accept the default, but a process can reset the default action with

## Slide 36: Signal Handling
Signal | 
Purpose | Simple signal handling
Include | #include <signal.h>
Usage | return = signal (int signum, void (*actin)(int))
Args | signum : the signal to respond to action : how to respond
Returns | -1 : if error preaction. : if success
Notes: The play_again3 program would be better if, upon receiving SIGINT, it called a function to restore settings and then exit().
To install a signal handler, a program calls signal(signum, functionname);
signal(signum, functionname); call allows exactly this sort of response

## Slide 37: Example of Signal Handling
Ex 6: Catching a Signal

## Slide 38: Example of Signal Handling

## Slide 39: Example of Signal Handling
Ex 7: Ignoring a Signal

## Slide 40: Example of Signal Handling
Interrupt signals (Ctrl + C)
QUIT signals (Ctrl + \)

## Slide 41: Contents
6.1 Software Tools vs. Device-Specific Programs
6.2 Modes of the Terminal Driver
6.3 Writing a User Program: play-again.c
6.4 Signals
6.5 Prepared for Signals: play_again4.c

## Slide 42: Ex 8: play_again4.c
Notes: It catches the keyboard signals and exits as if the user typed no.

## Slide 43: Ex 8: play_again4.c

## Slide 44: Ex 8: play_again4.c

## Slide 45: Ex 8: play_again4.c

## Slide 46: Summary
Some programs process data from specific devices. These device-specific programs have to control the connection to the device.
Terminal driver has many settings. A collection of setting is called a mode of the terminal driver. Programs for users often set the mode of the terminal driver.
A signal is a short message sent from the kernel to a process. Users, other processes, and the kernel itself may request a signal. A process tells the kernel how it wants to respond when it receives a signal.